## Slide 1
SSWT ZC467
Computer Networks
Contact Session – 5
Prabhu Subramanian

## Slide 2
IMP Note to Self

## Slide 3
CH5.1 = Multiplexing, Demultiplexing
CH5.2 = Sliding Window
CH5.3 = Flow and Error control; connectionless and connection oriented
Agenda

## Slide 4
Position of transport layer

## Slide 5
Transport layer create packet from the message received by the application layer
Packetizing - divides long message into smaller ones smaller ones are encapsulated into the data field of the TL packet and headers are added
Packetizing

## Slide 6
Connection-oriented delivery
    Establishes virtual path between sender & receiver
    Packets may travel in of order
    Transparent to communication in both direction
Connectionless Delivery
    Treats each packet independently
    No connection
Connection Control

## Slide 7
Packet carrying the request must specify to which server program the request must be delivered
PROVIDING RELIABILITY
Flow control
Error control
ADDRESSING

## Slide 8
Types of data deliveries

## Slide 9
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
Transport services and protocols
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 10
16 bit numbers ( between 0 and 65,535)
Client Program - ephemeral port - chosen randomly - transport layer software running on the client host
Server program - well known port numbers- Universal port numbers
Port numbers for Internet model

## Slide 11
Port numbers

## Slide 12
IP addresses versus port numbers

## Slide 13
Multiplexing, Demultiplexing
Sliding Window
Flow and Error control; connectionless and connection oriented
Transport Layer

## Slide 14
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
Transport services and protocols
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 15
Two principal Internet transport protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  reliable, in-order delivery
  congestion control
  flow control
  connection setup
UDP: User Datagram Protocol
  unreliable, unordered delivery
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees

## Slide 16: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg

## Slide 17: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
transport
Receiver:
app. msg
extracts application-layer message
checks header values
receives segment from IP
Th
app. msg
demultiplexes message up to application via socket

## Slide 18
Multiplexing/Demultiplexing
Transport
Layer
Network
Layer
Transport
Layer
Network
Layer
HTTP
FTP
Telnet
Use same communication channel between hosts for several logical communication processes
How does Mux/DeMux work?
  Sockets: doors between process & host
  UDP socket: (dest. IP, dest. Port)
  TCP socket: (src. IP, src. port, dest. IP, dest. Port)

## Slide 19
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Multiplexing / Demultiplexing

## Slide 20
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg
Multiplexing / Demultiplexing

## Slide 21
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg
Ht
Hn
HTTP msg
Multiplexing / Demultiplexing

## Slide 22
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
Hn
Multiplexing / Demultiplexing

## Slide 23
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client1
client2
P-client1
P-client2
Multiplexing / Demultiplexing

## Slide 24
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
Multiplexing / Demultiplexing

## Slide 25: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 26
UDP socket identified by two-tuple:
  (dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket
Connectionless demux

## Slide 27
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Connection-oriented demux
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 28
Principles of Reliable Data Transfer
important in application, transport, and link layers
Sending
Process
Receiving
Process
Reliable Channel
Sending
Process
Receiving
Process
Unreliable Channel
RDT protocol
(sending side)
RDT protocol
(receiving side)
Application Layer
Network Layer
Transport Layer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 29: Principles of reliable data transfer
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: note arrows through reliable data transfer channel is just one way – reliably send from sender to receiver

## Slide 30: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: Spend some time talking about how its to the sender and receiver side protocol that IMPLEMENTS reliable data transfer
Communication over unreliable channel is TWO-way: sender and receiver will exchange messages back and forth to IMPLEMENT one-way reliable data transfer

## Slide 31: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Complexity of reliable data transfer protocol will depend (strongly) on characteristics of unreliable channel (lose, corrupt, reorder data?)
Notes: So we have a sender side and a receiver side. How much work they’ll have to do depends on the IMPAIRMENTS introduced by channel – if the channel is perfect – no problem!

## Slide 32: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Sender, receiver do not know the “state” of each other, e.g., was a message received?
unless communicated via a message
Notes: Here’s a point of view to keep in mind – it’s easy for US to look at sender and receiver together and see what is happening. OH – that message sent was lost.
But think about it say from senders POV How does the sender know if its transmitted message over the unreliable channel got though?? ONLY if receiver somehow signals to the sender that it was received.
The key point here is that one side does NOT know what is going on at the other side – it’s as if there’s a curtain between them. Everything they know about the other can ONLY be learned by sending/receiving messages.
Sender process wants to make sure a segment got through. But it can just somehow magically look through curtain to see if receiver got it. It will be up to the receiver to let the sender KNOW that it (the receiver) has correctly received the segment.
How will the sender and receiver do that – that’s the PROTOCOL.
Before starting to develop a protocol, let’s look more closely at the interface (the API if you will)

## Slide 33: Reliable data transfer protocol (rdt): interfaces
sending process
data
receiving process
data
unreliable channel
sender-side
implementation of rdt reliable data transfer protocol
receiver-side
implementation of rdt reliable data transfer protocol
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
data
Header
data
Header
rdt_send(): called from above, (e.g., by app.). Passed data to deliver to receiver upper layer
udt_send(): called by rdt
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on receiver side of channel
deliver_data(): called by rdt to deliver data to upper layer
Bi-directional communication over unreliable channel
data
packet

## Slide 34: Reliable data transfer: getting started
We will:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow in both directions!
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions
use finite state machines (FSM) to specify sender, receiver
Notes: SO let’s get started in developing our reliable data transfer protocol, which we’ll call rdt (need a good acronym for protocol – like HTTP, TCP, UDP, IP)
Bullet points 1 and 2
NOW if we are going to develop a protocol, so we’ll need some way to SPECIFY a protocol. How do we do that?
We could write text, but as all know, that’s prone to misinterpretation, and might be incomplete. You might write a specification, and then think “oh yeah – I forgot about that case”
What we need is more formal way to specify a protocol. In fact, with a formal specification there may be ways to PROVE PROPERTIES about a specification. But that’s an advanced topic we won’t get into here. We’ll start here by adopting a fairly simple protocol specification technique known as finite state machines (FSM)
And as the name might suggest, a central notion of finite state machines is the notion of STATE
<talk about state>

## Slide 35: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 36
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
Reliable Data Transfer: FSMs

## Slide 37
rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L
rdt_send(data

## Slide 38
rdt3.0 in action

## Slide 39
rdt3.0 in action

## Slide 40
rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 41
Pipelining: Increased Utilization
Connectionless demux: example
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Increase utilization
by a factor of 3!

## Slide 42
Stop-and-wait allows the sender to only have a single unACKed packet at any time
example: 1 Mbps link (R), end-2-end round trip propagation delay (D) of 92ms, 1KB packet (L):
Pipelining: Motivation
T
transmit
=
8kb/pkt
10**3 kb/sec
= 8 ms
L (packet length in bits)
R (transmission rate, bps)
=
  1KB pkt every 100 ms -> 80Kbps throughput on a 1 Mbps link

## Slide 43
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols
  go-Back-N
  selective repeat
Pipelined protocols

## Slide 44
Allow up to N unACKed pkts in the network
  N is the Window size
Sender Operation:
  If window not full, transmit
  ACKs are cumulative
  On timeout, send all packets previously sent but not yet ACKed.
  Uses a single timer – represents the oldest transmitted, but not yet ACKed pkt
Go-Back-N

## Slide 45
1. [0, base-1] - packets that have already been transmitted and acknowledged
2. [base,nextsequence-1] - packets that have been sent but not yet ack
3. [nextseqnum, base+N-1] - packets that can be sent immediately
4. Seqnum > N+1 cannot be used until unack packet in the pipelimne is ack
4 intervals in the range of sequence numbers

## Slide 46
Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 47
GBN in action

## Slide 48
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACKed pkts
Selective Repeat

## Slide 49
Selective repeat: sender, receiver windows

## Slide 50
Selective repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore

## Slide 51
Selective Repeat Example
0123 456789
PKT0
PKT1
PKT2
PKT3
ACK0
ACK1
ACK2
ACK3
0 1234 56789
PKT4
0 1234 56789
PKT1
ACK1
ACK4
01234 5678 9
0 1234 56789
01 2345 6789
01234 5678 9
Time-Out
Sender
Receiver

## Slide 52
Another Example

## Slide 53
GBN in action